## Slide 1
Raman–DFT Analysis of N-Acetylmuramic Acid (NAM)
2D Structure
3D Structure

## Slide 2
Parameter | Range
Laser wavelength | 785 nm
Laser power | 10–80 %
Integration time | 10–25 s
Spectral range | 200–3000 cm⁻¹
Raman Measurement
DFT Simulation Parameters (NAM)
Software: Gaussian 16
Method: B3LYP / 6-31+G(d,p)
Calculation: Opt (Tight) + Freq (Raman)
Geometry: Connectivity defined
Resources: 16 cores, 56 GB RAM
Raman Data Processing
Spectra were preprocessed before analysis.
Processing pipeline:
Dark subtraction
Savitzky–Golay smoothing
Baseline correction (ALS)
Normalization
Peak detection
SNR calculation

## Slide 3
Optimal Raman Parameters
These settings produced the highest quality spectrum.
Parameter | Value
Integration time | 25 s
Laser power | 80 %
Best SNR | 95.9
> 80 = Excellent
SNR Interpretation:
>80 → Excellent
50–80 → Very Good
30–50 → Good

## Slide 4
Acquisition Parameter Analysis

## Slide 5
Raman Peak Assignments
Raman Shift | Assignment
1701 | C=O stretch
1546 | Amide II
1452 | CH₂ bending
1086 | C–O stretch
872 | C–O–C stretch
956 | Pyranose ring breathing
C=O stretch
C–O stretch

## Slide 6
Experimental vs DFT Raman Spectrum (NAM)
Excellent agreement between experiment and simulation (RMSE ~2 cm⁻¹) validates DFT for biomarker detection

## Slide 7
Simulation vs Literature Simulation
Your Sim (cm⁻¹) | Literature (cm⁻¹) | Error | Assignment
216.1 | 214.2 | ~2 | CH rocking
282.5 | 292.7 | ~10 | Torsion
562.4 | 558.9 | ~3 | C–O bending
1009.5 | 1010.5 | ~1 | C–O–C stretch
1260.1 | 1233.8 | ~26 | Amide III
1508.0 | 1535.1 | ~27 | Amide II
1652.7 | 1677.0 | ~24 | Amide I
1725.1 | 1763 / 1677 | ~40 | Carbonyl
Strong agreement with literature-reported DFT frequencies confirms reliability of the simulation method.
IMPORTANT MATCHES 1. 1009.5 ≈ 1010.5 cm⁻¹
Perfect match From literature: ν(C–O–C)
This is: NAM SIGNATURE PEAK (ETHER / LACTYL GROUP)
2. 1652.7 ≈ 1676 cm⁻¹
Amide I Confirms: N-acetyl group
3. 1508 ≈ 1535 cm⁻¹
Amide II 4. 1347 ≈ 1318 cm⁻¹ CH bending
ERROR ANALYSIS
Observations:
Low region (<1000): ~2–30 cm⁻¹
Mid region: ~20–40 cm⁻¹
High region: ~20–50 cm⁻¹
This validates your computational workflow.

## Slide 8
Experimental vs Simulation
The measured pure NAM powder spectrum shows strong agreement with theoretical vibrational modes across key fingerprint regions.
Experimental | Simulated | Difference | Assignment
284.3 | 282.5 | -1.8 | Ring deformation
772.7 | 777.8 | +5.1 | Ring / CH wagging
955.9 | 965.7 | +9.8 | Ring breathing
1155.4 | 1156.9 | +1.5 | C–O–C stretch
1249.4 | 1260.1 | +10.7 | C–N / OH deformation
1345.9 | 1347.4 | +1.5 | CH deformation
1451.8 | 1431.4 | -20.4 | CH₂ / CH₃ bending
1700.7 | 1725.1 | +24.4 | C=O stretch
Strong Matches (Excellent Agreement)
Peaks with very small shift (≈0–5 cm⁻¹):
284.3 ↔ 282.5
772.7 ↔ 777.8
1155.4 ↔ 1156.9
1345.9 ↔ 1347.4
This validates your real measured NAM powder spectrum.

## Slide 9
In the present study, Raman spectroscopy of high-purity N-acetylmuramic acid powder was used to establish the characteristic spectral fingerprint of NAM. Identification is based on the collective pattern of multiple Raman bands rather than any single peak, since individual vibrations may also appear in other biomolecules. Direct comparison with whole bacterial spectra is limited because bacterial samples contain proteins, lipids, nucleic acids, and other overlapping components. Therefore, the most appropriate validation is comparison between the experimental pure NAM spectrum and DFT-simulated NAM spectrum, where strong agreement was observed. The obtained pure NAM spectrum can now serve as a reference control for future analysis of complex biological or bacterial samples.
Larger Shifts
Observed in some peaks due to:
solid-state vs isolated molecule effects
hydrogen bonding
anharmonicity
basis set limitations
coupled vibrational modes
experimental environment
Conclusion

## Slide 10
Lipoteichoic Acid
Challenge in LTA Simulation
LTA is a large polymeric biomolecule
Full DFT simulation → computationally impractical
Need a scientifically valid alternative approach
Component-Based Modeling Strategy
“Fragment-based modeling is a standard approach for large biomolecules”
Decompose LTA into representative molecular units
Simulate each component using DFT
Combine spectral contributions to reconstruct LTA fingerprint
Lipoteichoic acid consists of three structural components:
• Glycolipid membrane anchor • Poly(glycerol–phosphate) backbone • Substituent groups such as D-alanine residues or sugars
Structure of Lipoteichoic Acid

## Slide 11
DFT Simulation Method
Quantum-chemical calculations were performed using Gaussian 16.
The simulation included:
• geometry optimization • vibrational frequency calculation • Raman activity calculation
Parameter | Value
Functional | B3LYP
Basis set | 6-31G(d)
Solvent model | SMD (water)
Gaussian keywords used:
# B3LYP/6-31G(d) Opt Freq Raman SCF=Tight Int=UltraFine SCRF=(SMD,Solvent=Water)
Explanation:
SCF=Tight ensures strict electronic convergence
Int=UltraFine improves numerical accuracy
SCRF=SMD models the aqueous environment in which LTA normally exists
DFT frequencies typically overestimate vibrational frequencies, so a scaling factor is applied.
Scaled frequency = frequency × 0.96

## Slide 12
The backbone is composed of repeating units:
glycerol – phosphate – glycerol – phosphate
Typical LTA molecules contain 10–20 repeating glycerol–phosphate units, producing large polymers with hundreds of atoms.
Because the full polymer is computationally expensive for quantum simulations, smaller molecular fragments are often used to represent the local chemical environment responsible for Raman-active vibrations.
General structure:
Lipid anchor – (Gro–P)ₙ
where: Gro = glycerol P = phosphate
LTA contributes to:
bacterial adhesion
cell wall maintenance
activation of host immune responses through receptors such as Toll-like receptor 2

## Slide 13
Modeling the LTA Substituent: D-Alanine
Why D-Alanine?
• Represents amino substituent in LTA • Responsible for surface charge regulation • Important for Gram-positive bacterial identification
Molecular Characteristics
• Exists in zwitterionic form: NH₃⁺ – COO⁻ • Contains:
        Amino group
        Carboxylate group
        Methyl group
DFT Simulation Method
• Geometry optimization + Raman calculation • Functional: B3LYP • Basis set: 6-31G(d) • Solvent: SMD (water)
2D Structure
3D Structure

## Slide 14
Modeling the LTA Substituent: GlcNAc
Why GlcNAc?
• Represents carbohydrate component • Present in bacterial cell wall structures • Provides strong Raman-active sugar signals
Molecular Characteristics
• Pyranose ring structure • Contains:
      Multiple hydroxyl groups (–OH)
      Acetamide group (–NHCO–)
      C–O–C linkages
DFT Simulation Method
• Geometry optimization + Raman calculation • Functional: B3LYP • Basis set: 6-31G(d) • Solvent: SMD (water)
3D Structure
2D Structure

## Slide 24
Background
Lipopolysaccharide (LPS) is a major component of Gram-negative bacterial outer membranes.
It is strongly associated with inflammation, endotoxemia, and sepsis.
Rapid identification of LPS-related spectral fingerprints can support diagnostic research.
Raman spectroscopy provides label-free molecular fingerprinting.
Problem Statement
Full LPS is structurally large and complex.
Direct spectral interpretation is difficult due to overlapping bands and multiple functional groups.
Objective
Acquire Raman spectra of LPS powder under optimized conditions.
Build fragment-based computational models representing major LPS substructures.
Compare simulated and experimental spectra.
Identify dominant contributors and characteristic Raman bands.

## Slide 25
Experimental Workflow
Sample: LPS powder
Raman measurements performed under multiple acquisition settings:
  Different integration times
  Different laser powers
  Different accumulations
Best experimental condition selected based on signal quality and reproducibility.
Optimized Condition Chosen
60 s integration
20% laser power
30 accumulations
Computational Workflow
Representative fragments selected:
KDO
Heptose
D-Glucosamine
Myristic Acid
Phosphoric Acid

## Slide 26
Simulation Method
Geometry optimization
Frequency + Raman calculations
DFT using B3LYP / 6-31G(d)
Data Processing
Interpolation to common Raman grid
Normalization
Composite model generation:
  Equal-weight model
  NNLS optimized model