## Slide 1
Rapid Extraction of Bacterial Cell-Wall Biomarkers from Human Blood for SERS-Based Sepsis Detection
Targets:
LPS (Gram-negative marker)
LTA (Gram-positive marker)
NAM (Universal bacterial cell-wall marker)
Clinical Need
Blood culture requires 12–72 hours.
Early sepsis treatment needs faster identification.
Direct biomarker detection from blood can reduce diagnostic delay.
SERS offers rapid and sensitive molecular fingerprinting.
Project Objective
To develop a rapid workflow for:
Blood sample preprocessing
Extraction/enrichment of LPS, LTA and NAM
SERS-based detection
Future AI-assisted classification
Target turnaround time: less than 1 hour.

## Slide 2
Overall Workflow
Blood collection
Plasma separation / RBC lysis
Debris removal
Target-specific enrichment
Sample cleanup
SERS measurement
Data analysis
Blood Collection and Primary Processing
Sample: 5–10 mL venous blood Preferred tube: K2-EDTA / Heparin (assay dependent)
  Why important:
  Prevents clotting
  Preserves biomarkers
  Minimizes degradation
  Pre-analytical conditions affect recovery
Processing time: 5 minutes

## Slide 3
Plasma Separation / RBC Lysis
Option A: Plasma Separation
Centrifuge: 2000 g, 10 minutes
Collect plasma for soluble biomarkers
Debris Removal and Cleanup
Methods:
Secondary centrifugation
0.22–0.45 µm filtration
Washing with saline / DI water
Protein reduction by dilution or protease treatment
Purpose:
Remove cells and debris
Reduce hemoglobin and protein interference
Improve SERS signal quality
Option B: RBC Lysis
Dilute blood 1:10 with sterile water
Hypotonic shock lyses RBCs
Releases trapped bacteria/biomarkers

## Slide 4
LPS Extraction Strategy
Target: Lipopolysaccharide (Gram-negative)
LTA Extraction Strategy
Method:
Anti-LTA antibody functionalized beads/substrate
  Workflow:
  Add capture beads
  Incubate 10 minutes
  Magnetic separation
  Wash and resuspend
  Transfer for SERS
Method:
Polymyxin B or anti-Lipid A functionalized magnetic beads
  Workflow:
  Add capture beads
  Incubate 10 minutes
  Magnetic separation
  Wash and resuspend
  Transfer for SERS
Target: Lipoteichoic Acid (Gram-positive)

## Slide 5
NAM Extraction Strategy
Target: N-Acetylmuramic Acid
Key Matrix Challenges
Blood interferents:
Albumin
Lipoproteins
Hemoglobin
Salts
Host defense peptides
Method 1:
Protein removal + direct detection
Method 2:
Mild hydrolysis of peptidoglycan fragments to release NAM-related species
  Workflow:
  Protease treatment or hydrolysis
  Centrifuge cleanup
  Collect supernatant
  Transfer for SERS
Impact:
Target masking
Reduced recovery
Signal variability
Solution:
Rapid processing
Cleanup chemistry
Affinity enrichment

## Slide 6
SERS Detection Step
Sample preparation:
Mix extracted analyte with Au/Ag nanostructures
Incubate 2–5 minutes
Deposit on substrate
Typical measurement:
Laser: 785 nm
Integration: 10 s
Range: 500–2000 cm^-1
Output: Unique Raman fingerprint of biomarker
Estimated Total Time
Collection: 5 min
Separation/Lysis: 10–15 min
Cleanup: 10 min
Enrichment: 15–20 min
SERS Prep + Scan: 10 min
Total: 45–60 minutes
Compared with blood culture: 12–72 hours

## Slide 7
Novel Findings from Literature
Anticoagulant choice changes measurable biomarker levels.
Delayed processing reduces detectable endotoxin.
Surfactant + heat improves LPS recovery.
Protease + low pH reduces matrix interference.
Extracellular vesicles may carry LPS/LTA.
Direct NAM detection remains underdeveloped.
Research Significance
Rapid sepsis screening
Differentiation of Gram-negative vs Gram-positive infection
Universal bacterial detection using NAM
Compatible with portable diagnostics
Potential for ICU and neonatal care

## Slide 8
Future Scope
Conclusion
A successful blood biomarker biosensor requires:
Robust sample preparation
Efficient target enrichment
Strong SERS substrate design
Reliable spectral analysis
Combining these steps can enable rapid and clinically useful sepsis diagnostics.
Integrated microfluidic cartridge
Multiplex detection of LPS + LTA + NAM
AI-based spectral classification
Point-of-care handheld device
Clinical validation with patient samples

## Slide 9
Future Scope
1. Boardman AK et al. (2016)
Rapid Detection of Bacteria from Blood with Surface-Enhanced Raman Spectroscopy Key Highlight: Demonstrated direct recovery of bacteria from blood followed by SERS identification without waiting for blood culture. Showed feasibility of rapid bloodstream infection detection.
2. Hassan M. et al. (2024)
Recent Advances in Bacterial Detection Using Surface-Enhanced Raman Scattering Key Highlight: Comprehensive review of modern SERS platforms for bacterial sensing, substrate design, machine learning integration, and clinical challenges.
3. Verde A. et al. (2021)
SERS Sensing of Bacterial Endotoxin on Gold Nanoparticles Key Highlight: Label-free detection of LPS using gold nanostructures. Validated that endotoxin can be directly sensed using plasmonic platforms.
4. Liu L. et al. (2023)
Recent Progress of Surface-Enhanced Raman Spectroscopy for Bacteria Detection Key Highlight: Summarized recent progress in bacterial detection, portable Raman systems, microfluidics, and signal enhancement strategies.
5. Rapid Microbial Sample Preparation from Blood Using a Novel Concentration Device
Key Highlight: Developed selective lysis and concentration workflow to isolate microorganisms from large blood volumes into a small final sample volume.
6. Simple Dual Filter Workflow for Facilitating Blood Culture-Free Detection
Key Highlight: Introduced dual filtration strategy to remove blood debris and capture bacteria for downstream analysis.
7. Rapid Separation of Bacteria from Blood—Review and Outlook
Key Highlight: Compared multiple blood preprocessing methods including lysis, centrifugation, filtration, and microfluidic separation.
8. Interferences from Blood Collection Tube Components on Clinical Chemistry Assays
Key Highlight: Showed that anticoagulant and tube additives affect analytical results, emphasizing importance of sample collection conditions.
9. Dynamic Profiling of Lipoteichoic Acid (LTA) and/or Lipopolysaccharide (LPS) Positive Extracellular Vesicles in Plasma as Diagnostic and Prognostic Biomarkers for Bacterial Infection
Key Highlight: Demonstrated that bacterial extracellular vesicles carrying LPS/LTA can act as diagnostic and prognostic biomarkers in plasma.
10. Peptidoglycan and Lipoteichoic Acid from Staphylococcus aureus Induce TNF-α, IL-6, and IL-10 Production
Key Highlight: Established the biological inflammatory significance of LTA and peptidoglycan in host immune activation.

## Slide 10
11. A Detailed Guide for Metabolic Incorporation of N-Acetyl Muramic Acid Probes into Bacterial Peptidoglycan
Key Highlight: Validated NAM as a specific bacterial cell-wall target and described methods to track it in bacterial systems.
12. Protected N-Acetyl Muramic Acid Probes Improve Bacterial Peptidoglycan Incorporation via Metabolic Labeling
Key Highlight: Improved NAM probe incorporation efficiency, supporting NAM-targeted diagnostics.
13. Imaging the Bacterial Cell Wall Using N-Acetyl Muramic Acid-Derived PET Radiotracers
Key Highlight: Demonstrated diagnostic value of NAM-derived molecules for bacterial imaging.
14. Charge-Engineered LPS-Targeting Magnetic Nano-adsorbents with Anti-Fouling Properties
Key Highlight: Designed anti-fouling magnetic materials that selectively capture LPS even in protein-rich samples like plasma.
15. Rapid Magneto-Enzyme-Linked Immunosorbent Assay for Ultrasensitive Protein Detection
Key Highlight: Showed magnetic bead-based immunocapture can accelerate and improve sensitivity of biomarker assays.
16. Microfluidic SERS Devices: Brightening the Future of Bioanalysis
Key Highlight: Reviewed integration of SERS with lab-on-chip systems for automated and portable diagnostics.
17. Recent Developments in SERS Microfluidic Chips: From Fundamentals to Biosensing Applications
Key Highlight: Covered recent microfluidic chip designs for biosensing and rapid sample handling.
18. Rapid (<5 min) Identification of Pathogen in Human Blood by Electrokinetic Concentration and SERS
Key Highlight: Achieved very fast pathogen concentration and detection from blood using electrokinetic microfluidics combined with SERS.
19. SERS-Based Biosensors Combined with Machine Learning for Medical Application
Key Highlight: Demonstrated how PCA, LDA, and machine learning improve interpretation and classification of Raman biosensing data.
20. A Surface-Enhanced Raman Spectroscopy-Based Biosensor for the Detection of Biological Macromolecules: The Case of Lipopolysaccharide Endotoxin Molecules
Key Highlight: Specific case study of LPS detection using SERS biosensor architecture with quantitative